# Abstract
The RISC-V instruction set architecture (ISA) has been designed to be highly modular and customizable through the use of extensions. This makes it an ideal platform for processor formal verification, which is a critical step in the design of processor cores. This report presents the formal verification of the PAF Core that was used as the basis for this research. This core is an open-source RISC-V processor core written as a university project at Telecom Paris by Florian Tarazona and Erwan Glazsiou. The PAF Core was found to be quite buggy and in need of significant modifications to be compatible with the riscv-formal tool, which is used to prove that a processor is correct according to the RISC-V ISA.
The formal verification of the PAF Core covered the base RISC-V ISA (rv32i) and the B extension (Bit manipulation). The core was modified to implement trapping, which detects ill-formed instructions and unaligned accesses. Several bugs were found and fixed such as missing instructions, pipeline stalls not properly implemented, bad forwarding and load instruction triggering trap on miss-aligned addresses.
In addition to the formal verification of the PAF Core, the report also includes the formal verification of an AXI-lite random memory controller, which I used to formally verify AXI-lite variant of the picorv32 core.
The report concludes with an analysis of the contributions of the research, including a timing and area analysis of the PAF processor. The results of this work provide a strong foundation for further improvements to the PAF Core.
# Introduction
## formal verifications for processor cores
Verification is a critical step in processor design. It was in the 1990s, as for the MIPS 4000, each additional month of design time would cost between $3 million and $8 million. Besides, 27% of the design time was devoted to verification and testing[3]. It is still the case, nowadays the verification process has become considerably more extensive than design efforts[4].
Most bugs can be found using simulation based verification: The design under test is simulated in a testbench that gives inputs and checks coherency of the design’s outputs.
Another method that is usually used to find more bugs is to simulate the design, with randomly generated inputs. This method can find cases the usual testbench doesn’t consider, thus find more bugs. This function is efficient at finding bugs though it does not give any proof of correctness. Even after simulating during days on random inputs, one untested input can still lead to a state that violates the specification.
This is where formal verification comes to play. it is a process of mathematically proving the correctness of a design, in this case, a processor design. The verification process of the pentium 4 involved formal verification, which made possible to find around 200 bugs that weren’t emphasized by simulation based verification methods.
The principle of hardware formal verification is to define a formal specification of the design, and then use mathematical logic and automated theorem provers to prove that the design meets that specification. This can provide a high degree of confidence that the design is free from certain classes of errors and will function as intended.
The first step is to define a formal specification of the design. This typically involves writing a mathematical model of the design that defines its behavior in terms of input and output relations. The model is usually written in a formal language, such as first-order logic or temporal logic.
There are serval verification methodologies, such as model checking and theorem proving. While theorem proving gives stronger proofs of correctness, it is difficult to automate and highly relly on the design under verification.
Model checking works by exhaustively exploring the state space of the system under consideration and looking for a state that violates the specification. In model checking, a mathematical model of the system is created, and a formal specification is defined in terms of properties that the system should satisfy. The model checker then explores the state space of the system, using algorithms to check that the system satisfies the specification. Model checkers can check both safety properties (properties that must always hold) and liveness properties (properties that eventually hold).
Unbounded model checking searches for any reachable state that violates the specification. It usually target small systems for which the set of reachable states is handlable, whereas it is not for big end-to-end systems, like advanced processor cores. Indeed, the size of the set of reachable states grows exponnentially with the size of the system. Thus, bounded model checking is often used instead to find bugs. The principle is to restrict the set of states to check to the set of reachable states after a few clock cycles. The number of considered clock cycles usually depends on the pipeline depth of the processor core. This method is sometimes called bug hunting: it does not prove correctness of the design overtime, though, this method is still very efficient at finding bugs.
The model checking problem is equivalent to a satisfiability (SAT) problem. Model checkers usually create a logic formula that should be unsatifiable if and only if the design is correct. It then involves a SAT solver to prove that the formula is unsatisfiable and thus prove correctness of the design. Modern model checkers speed up the solving process by construsting a SMT problem instead of a SAT one.
#### Limits of model checking
The SAT problem is NP-complete in the worst case. It means that checking that a vector of variables satisfy a formula is possible in a polynomial time. Though finding such a vector is only possible in exponential time in the worst case.
While most SAT problem instances doesn’t need an exponential time, which makes possible the use of such a tool for formal verification, some logical structures actually take an exponential time to verify.
It is the case for multipliers, divisors, and for some floating points operators. It means that bounded model checking cannot be used to prove correctness of such such circuts.
Verifying very big end-to-end systems can also not be achievable. It is usual to verify parts of such systems independently instead. For example, for a processor core, formally verifying the ALU, the register file and other parts independently is easier than verifying the whole core.
## riscv-formal
The work presented in this report is based on the open source riscv-formal tool. It is an open source tool to formally verify RISC-V processor cores. It is written in the SVA (SystemVerilog Assertions) language and uses the SymbiYosys verification tool to perform the formal verification. It is based on the bounded model checking method, and use SymbiYosys to generate and solve a SMT problem.
In order to be verified using this tool, a core must implement the RISC-V Formal Interface (RVFI). It is a set of signals that a core must export to make visible its behaviour.
It is a set of signals and a protocol introduced by riscv-formal, that allows formal verification tools to access and interact with the internal state of a RISC-V core. This interface exposes the behavior of the core in a way that can be easily understood and verified by formal verification engines. These signals include the inputs and outputs of the core, as well as internal signals such as register values and memory states. RVFI can be used for a variety of formal verification tools and methodologies.
Figure 1 shows a subset of the RVFI signals, for a 32 bit RISC-V core.
When valid is asserted, an instruction is executed and the other signals are set. insn indicates the executed RISC-V instruction. pc_rdata is set to the instruction’s PC, and pc_wdata is set to the next instruction’s PC - PC + 4 or a jump address if the instruction is a branch, or a trap handler if the instruction traps. Every instruction is associated with a unique order value, in order to verify the sequencial consistency of a core. If the instruction uses registers, rs*_rdata and rd_rdata are set to the decoded addresses. If the instruction reads data from memory, mem_addr is set to the associated address, and mem_rdata is set to the read word. mem_addr and mem_wdata are set similarly in case the instruction operates a memory write. If the instruction traps, trap is set.
Note that the RVFI interface doesn’t support instructions that both read and write from memory, or reads / writes twice. It is not a problem to verify the base ISA and most standard extension in which every instruction does at most one read or one write. Some modifications are however needed to verify the Atomic “A” standard extension, as it introduces atomic read then write instructions, like AMOADD - Atomic Memory Operation Add. To verify this extension, some extra signals are added to RVFI.
name	size (bits)	meaning
valid	1	indicates whether the current instruction is valid or not. Every other signal is only valid when rvfi_valid is asserted.
order	64	order of the instruction
insn	32	binary instruction that is currently being executed
trap	1	indicates if the current instruction is a trap instruction or not
rs1_addr	5	address of the first source register (RS1) that is used by the instruction, if any
rs1_rdata	32	the value of the first source register (RS1) that is used by the instruction, if any
rs2_addr	5	address of the second source register (RS2) that is used by the instruction, if any
rs2_rdata	32	contains the value of the second source register (RS2) that is used by the instruction, if any
rd_addr	5	address of the destination register (RD) that is used by the instruction, if any
rd_wdata	32	value that will be written to the destination register (RD) by the instruction, if any
pc_rdata	32	current value of the program counter (PC)
pc_wdata	32	new value of the program counter (PC) after the instruction is executed (PC + 4 or a jump address)
mem_addr	32	memory address that is being accessed by the instruction, if any
mem_rdata	32	value read from memory by the instruction, if any
mem_wdata	32	value that will be written to memory by the instruction, if any

Figure 1 - subset of the RVFI signals, for a 32 bit RISC-V core
As explained earlier, some operations are to hard to verify formally using the bounded model checking methodology. It is the case for the multiplication and division. it means that the Multiplier “M” standard RSC-V extension cannot be fully verified easily. The solution brought by riscv-formal is to replace such operations by alterative ones for instructions that cannot be verified in a reasonable time. It expects the processor under test to implement these alternative operations instead of the standard multiplication and division operations. Commutative operations like multiplication are replaced with addition followed by applying XOR with a bitmask that indicates the type of the operation. Noncommutative operations like division are replaced with subtraction followed by applying XOR with a bitmask that indicates the type of the operation. The bitmasks are 64 bits wide. RV32 implementations only use the lower 32 bits of the bitmasks.
Note that using alterative operations, no proof of correctness is given to the instruction. Other verification methods should then be used. The reason to use riscv-formal in such a case is that the only part that is not virified to be correct is the multiplier or the divisor. If the processor under verification uses a multiplier and a divisor that are already verified to be correct, it is not a problem.
The riscv-formal verification procedure is divided into serval tests. The tests required to prove bounded correctness of the processor (liveness and safety) are:
- liveness - this test checks that the core never freezes unless it halts.
- safety tests
  - Consistency checks: this set of tests aims to prove the consistency of sequences of instructions.
    - reg - prove that every register read return the previously written value.
    - pc_fwd - prove consistency of the PC.
    - unique: check that every retired instruction’s order is unique and increasing.
  - insn_* - instruction check: One check is generated for each instruction in the isa. It compares the instruction decoding, result and whether it traps or not to the behaviour described in the ISA.
  - out of order checks:
    - causal - check causality of instructions: if depends on the result of , then is retired after .
    - pc_bwd - prove consistency of the PC in an out of order context.
As is, riscv-formal is able to verify the following Instruction Set Architectures (ISAs): - rv32i: base 32 bit ISA - rv64i: base 64 bit ISA - rv32im: base 32 bit ISA with multiplier - rv64im: base 64 bit ISA with multiplier
Note that the tool is extensible for other ISA extensions. Adding the support to an ISA means generating one check per introduced instruction. This report include the support for the rv32ib as an example.
## Contributions
In this report are presented three contributions:
- A random memory AXI-lite slave that ingore writes and reads random values, that yosys interprets as symbolic values. The response times are also randomized, to test the AXI-lite specification. This slave has been used to foramlly verify the AXI-lite varient of the picorv32. This contribution is described in section ?.
- The support of the Bit Manipulation “B” RISC-V extension for the risv-formal tool for 32 bit processors. This contribution is described in section ?.
- The formal verification of the PAF Core, an open-source RISC-V processor core written as a university project at Telecom Paris. This included the modification of the core to implement trapping, which detects ill-formed instructions and unaligned accesses, as well as the detection and fixing of several bugs. The formal verification of the PAF Core covered the base RISC-V ISA (rv32i) and the B extension (Bit manipulation) and the results of this work provide a strong foundation for further improvements to the PAF Core. This contribution is described in section ?.
## Overview of the PAF Core
Figure 1 shows a simplified diagram of the implementation. It is a simple 5 stage pipelined core: - Instruction Fetch (IF): Fetches the instruction in data memory - Instruction Decode (ID): the instruction is decoded to determine its opcode and operands. - Execute (EX) the instruction is executed. This typically involves performing calculations or memory accesses based on the instruction and its operands. - Memory Access (MEM): In this stage, memory accesses specified by the instruction are performed. This includes reading or writing data from memory.
Figure 1 - simplified PAF core implementation diagram
## Bugs and fixes in the PAF Core
As the basis for this research on RISC-V extension formal verification, I needed a RISC-V core that was not formally verified. I picked the PAF core, written by Florian Tarazona and Erwan Glazsiou, students at Telecom Paris in 2021 for a univeristy project. However, the core was found to be quite buggy and in need of significant modifications in order to be compatible with the riscv-formal tool, which is used to prove that a processor is correct according to the RISC-V ISA.
### Initial modifications
The first modification made to the PAF core was the implementation of trapping, which detects ill-formed instructions and unaligned accesses. This change was necessary in order for the core to pass the riscv-formal formal tests.
ill-formed instructions are detected in the ID pipeline stage, and miss-align exceptions are detected in the EX stage. When a trap happens, the pipeline is flushed and the core halts.
Besides, some instructions went missing: - AUIPC - Add Upper Immediate to PC - is an instruction that allows the program counter (PC) to be modified by adding an upper immediate value to it. This instruction is typically used to facilitate the loading of program addresses into registers, allowing for program branching and subroutine calls. - LB, LH, LBU, LHU - These instructions are used to load a - SB, SH - These instructions are used to store a single byte or half word (two bytes)
Implementing the missing load/store instructions required to include byte masks in the memory interface, which was not done already.
For writes, a shift is required before sending the word to memory. It is done in the EX stage. A similar shift is also required for reads, which is done in the WB stage.
### Bugs found and fixes
Missing instructions for accessing memory bytes and half-words: New instructions were implemented. Add write strobe mask to the core’s data memory interface: The write strobe mask was added to the core’s data memory interface. JALR instruction clearing the last two bits: The instruction was modified to properly align the jump target address. Registers being latches: The implementation was changed to use registers that correctly hold the state of the processor. No detection of ill-formed instructions: New code was added to detect and trap these instructions. Pipeline stalls not properly implemented when load instruction followed by another instruction: The implementation was changed to properly handle the forwarding of load results to other instructions that use them. Bad forwarding from memory to execution stage: The forwarding mechanism for JAL, JALR and AUIPC instructions was modified. Load instruction triggers trap on miss-aligned addresses: The implementation was changed to avoid triggering a trap in these cases. BGE and BGEU instructions branch if strictly greater: The instructions were modified to branch if greater or equal. AUIPC instruction not implemented: The instruction was added to the core. JAL instruction not trapping when branch value is miss-aligned: The JAL instruction was modified to properly trap in these cases. Random memory errors: Future work could be directed to address these bugs. Overall, these modifications allowed the PAF core to pass the riscv-formal formal tests and fully implement the ‘B’ extension.# Implementation and verification of the RISC-V “B” extension
## Overview of the extension
The goal of the RISC-V Bit Manipulation ISA extension is to accelerate some operations that are regularily executed in common RISC-V code. It is divided into three subextensions, for a total of 31 instructions (and 12 other instructions for rv64).
### Zba (Array Indexing)
The Zba instructions are designed to accelerate the generation of addresses that index into arrays of basic types (halfword, word, doubleword). These instructions allow the addition of a shifted index to a base address. The shift amount is limited to 1, 2, or 3 but can be used to index arrays of wider elements by combining with the slli instruction from the base ISA.
### Zbb (Basic Bit-Manipulation)
The Zbb instructions provide basic bit-manipulation operations such as logical with negate, counting leading/trailing zero bits, counting population, finding integer minimum/maximum and sign- and zero-extension. These operations can be used to improve performance, reduce code size and energy consumption in applications.
### Zbc (Carry-less Multiplication)
The Zbc extension provides carry-less multiplication, a multiplication operation in the polynomial ring over GF(2). This extension includes instructions clmul and clmulh to produce the lower and upper half of the carry-less product respectively. The instruction clmulr produces bits 2✕XLEN−2:XLEN-1 of the carry-less product. This extension can be used for efficient cryptography and hashing operations.
## Verification
As explained in the introduction, riscv-formal allows to add ISA extensions by adding one check for each introduced instruction. Checks are generated in the python script /insn/generate.py. This script allows to easily describe an instruction, given its encoding and its result. A SyemVerilog verification file is generated for each instruction. Figure 3 shows the example for the ADDI and ADD instructions.
insn_imm("addi", "000", "rvfi_rs1_rdata + insn_imm")
...
insn_alu("add", "0000000", "000", "rvfi_rs1_rdata + rvfi_rs2_rdata")
Figure 3: generation of checks for instructions ADDI and ADD
The check’s computation is made naive and compared to the more complex implementation in the core. The resulting file can be found on the github sub repository, which has been forked an modified from the original YosysHQ repository.
## Implementation
### Zba
The Zba extension only has three instructions that add a shifted integer to another integer: SH1ADD, SH2ADD and SH3ADD. They are implemented using the regular ALU’s full adder that is already used for the ADD and ADDI instructions, by adding a barrel shifter.
### Implementing Zbb
Simple Zbb operations are implemented naively: logical and, or and xor with negate, reverse byte order, byte granule bitwise OR-Combine, and sign- and zero- extend operations. Other instructions required area and timing considerations to be efficiently implemented.
### Population count openrations
Operations that count bits (cpop, ctz and clz) are done in a single cycle. the data path for the computation is a tree that operates on a part of the word, and compresses to give the result.
### rotate operations
Zbb introduces ROL and ROR instructions. A left shifter and a right shifter were already in the ALU to implement the SLL and SLR instructions. To reduce the area cost of the extension, the left shifter and the right shifter are also used for the ROL and ROR ALU operations. Indeed, the bit rotate right of A by B is equal to: (A << B) | (A >> (32 - B)). Likewise, the bit rotate left of A by B is equal to: (A >> B) | (A << (32 - B)). By multiplexing the inputs of the shifters, they are made sufficent to implement every shift and rotate instructions.
### single bit operations
Zbb introduce single bit operations: BCLR, BCLRI, BEXT, BEXTI, BINV, BINVI, BSET and BSETI. These operations can be implemented using the left and right shifters as for ROL and ROR:
- BCLR A, bit n: A & ~(1 << n)
- BINV A, bit n: A ^ (1 << n)
- BSET A, bit n: A | (1 << n)
- BEXT A, bit n: (A >> n) & 1
### integer minimum / maximum
The base rv32i ISA includes the instructions BLT - Branch if Less Than, BGE - Branch if Greater or Equal, SLT - Set if Less Than, and their unsigned equivalents: BLTU, BGEU, and SLTU. Therefore, the ALU already contains the logic for integer comparisons.
The Zbb integer min/max are MAX, MAXU, MIN, MINU. They all were implemented use the comparaison logic already introduced to minimize the area cost.
### Zbc
Zbc clmul and clmulh are implemented using a parametrized N-cycle carry less multiplier that outputs the 64 bit product. clmulr gives the result of clmul shifted left by one bit. # Formal AXI slave
Model checking works in such a way that memory reads must be formally randomized. Indeed, a proof of correctness for a core means that it does not violates the specification, no matter the code it executes and the data it reads.
The riscv-formal tool puts symbolic inputs for each cycle and signal. The space of inputs can then be restricted by adding hypotheses, such as SystemVerilog assumptions.
The tool provides example of cores to verify, using a wrapper which generates symbolic inputs respecting the memory protocol. For every example the tool provides, the native memory interface is always quite simple. Figure ??? gives the example for the picorv32 memory interface.
input/output signal	size	meaning
output	1	mem_valid
output	1	mem_instr
input	1	mem_ready
output	32	mem_addr
output	32	mem_wdata
input	32	mem_rdata
output	4	mem_wstrb

Figure ??: picorv32 native memory interface
The protocol has a single read/write channel and only two inputs. Therefore it is not hard to meet the specification in this case. The example puts random values in both mem_rdata and mem_ready at every clock cycle.
However, some processor cores export more complex native memory interfaces. For example, in a real-case System-On-Chip with no cache, the core is often connected to an AHB, APB or AXI-lite bus atrbitrer. This fact motivates the need of a formal memory slave.
The picorv32 is available in 3 different versions:
- picorv32, wich uses the native memory interface presented on figure ??.
- picorv32_axi, which uses an AXI-lite memory interface.
- picorv32_wb, which uses a WhishBone memory interface.
This project provides the way to verify a core with a AXI-lite memory interface. The solution was to write a memory slave which reads symbolic values and ignores writes. To take memory stalls in consideration and potentially find associated bugs, the slave responds in a random time.
## AXI-lite protocol
AXI-lite is a light-weight adaptation of the ARM’s Advanced eXtensible Interface protocol. It introduces the concept of master, slave, channels and handshakes. The master is the initiator of the requests. It asks the slave to read or to write and the slave acknowledges.
AXI-lite provides the following channels:
- Address Read
- Read Response
- Data Write
- Address Write
- Write Response
While the Address Read, Address Write and Data Write channels are driven by the master, the Read Response and Write Response channels are driven by the slave. The channel driver controls a VALID sigal while the other end controls a READY signal. A transaction happens in a channel whenever both VALID and READY are asserted at the same time during one cycle. It is called a handshake.
A read sequence happens when a handshake on the Read Response Channel follows a handshake on the Read Address Channel.
A write sequence happens when handshakes on the Address Write and Data Write channels are followed by a handshake on the Write Response channel. Figure ?? shows the main AXI-lite signals.
Figure ?? and ?? show the dependancy between the channels for read and write sequences.

Address Read Channel
name	size (bits)	driver	meaning
ARVALID	1	master	valid signal
ARREADY	1	slave	ready signal
ARADDR	32	master	read address

Read Response Channel
name	size (bits)	driver	meaning
RVALID	1	slave	valid signal
RREADY	1	master	ready signal
RDATA	32	slave	read data
RRESP	2	slave	read response (for errors)

Address Write Channel name | size (bits) | driver | meaning – |– |– |– AWVALID | 1 | master | valid signal AWREADY | 1 | slave | ready signal AWADDR | 32 | master | write address
Data Write Channel
name	size (bits)	driver	meaning
WVALID	1	master	valid signal
WREADY	1	slave	ready signal
WDATA	32	master	write data
WSTRB	4	master

Write Response Channel
name	size (bits)	driver	meaning
BVALID	1	slave	valid signal
BREADY	1	master	ready signal
BRESP	1	slave	write response (for errors)

Figure ??: AXI-lite signals

fig23
Figure ??: Read transaction handshake dependencies, from the AXI Specification[6]

fig24
Figure ??: Write transaction handshake dependencies, from the AXI Specification[6]
## Implementation
riscv-formal provides a way to generate N bit symbolic registers - Registers that can potentially hold any possible value at every clock cycle. The slave is based on the use of these registers. However the AXI-lite specification requires the following main properties for a slave:
- P1 - RDATA and RRESP must be stable while RVALID is asserted.
- P2 - BRESP must be stable while BVALID is asserted.
- P3 - RVALID must eventually rise after a handshake on the address read channel.
- P4 - RVALID must only rise after a handshake on the address read channel.
- P5 - BVALID must eventually rise after a handshake of both the write and address write channels.
- P6 - BVALID must only rise after a handshake of both the write and address write channels.
The ARREADY, RVALID, AWREADY, WREADY and BVALID signals are symbolic and still
RRESP and BRESP are not used by the picorv32_axi core, so they are not geneated by the slave. However, a core could make use of these signals to generate memory access exceptions. For such a core, it would be usefull to give it a symbolic value when RVALID and respectively BVALID are asserted.
## Verification
The random slave has been first verified in simulation, using Mentor Questa Simulator and random values. As stated in the introduction section, simulation-based verification is not enough to provide a proof of correctness, so the slave has then been formally verified using unbounded model checking. The Mentor Verification tool ran SystemVerilog assertions and proved P1 - P6. Note that the verification module has been done as a part of a University lab at Telecom Paris.
## Liveness conditions
As an example of use, the picorv32_axi core is verified using presented formal axi-lite slave. See the git repository for instruction to reproduce the verification.
Note that this method won’t provide a proof of correctness for the AXI-lite port. A formal checker can be used conjointly to prove it.
The riscv-formal liveness check requires stronger assumtions on the memory interface. Indeed, the slave can take an arbitrary time to response. The verification wrapper is modified so that memory transactions take at most 9 clock cycles. The liveness check is passed using this value, for a symbolic execution of 30 clock cycles.
# Conclusions
## PAF rv32ib synthesis
This sections presents the synthesis of the PAF core. The synthesis is made using Altera Quartus 2020, targeting the Cyclone V 5CSEMA5F31C6 FPGA.
The core’s carry less multiplier takes N cycles where N is a synthesis parameter. It allowed to test multiple values and compare the timing and area cost between values.
### Timing analisys
The Quartus timing analysis showed that the critical path of the design is the following:
- data read register
- WB shift (LB/LH)
- WB->EX forwarding
- EX ADD rs1 + imm12
- new PC register
It means that the implentation of the bit manipulation extension does not decrease the timing performance, even with a single cycle carry less multiplier. The critical instruction sequence that lead to this data path being used is the showed on figure 4.
It is notable that this sequence is actually never executed in common code. Indeed, it is usual to load a address from memory and then jump to it, though an address is usually a word rather than a byte.
# Load a byte from memory, zero extend it
# and save it to r1
LB r1, r2, $0

# jump to the address in
JALR r0, r1, $0
Figure 4: critical instruction sequence
Despite these dependencies, the design was able to achieve a frequency of 87 MHz. However, the write-back shifter used for the LB and LH instructions was found to be quite expensive, adding 1.5 ns to the critical path and potentially leading to a loss of 10 MHz.
### Area analisys
Figure 5 shows the synthesis area results, for the core supporting rv32i. Figure 6 shows the synthesis area results for the core when supporting rv32ib, with a 4-cycle carry-less multiplier. The 4-cycle clmul is a trade-off between speed and area. Indeed, a core with single-cycle clmul takes around 20% more space for this target, as shows Figure 7.
Note that for the rv32i implementation, the EX stage module represents 79% of the total area. It hides the fact that the EX module hosts the register file. Besides, the instruction decoding is quite poor, which explains why the ID stage takes so few ALUTs compared to other stages. It might decrease the total area size to improve the instruction decoding in the ID stage.
We can see that the cost for the “B” extension is 36% of the total core area for a 4-cycle clmul.
Module hierarchy	cumulated ALUTs used by the module and submodules	ALUTs used by the module
top	1569.5	129.9
top:EX	1237.0	1237.0
top:ID	10.2	10.2
top:IF	75.3	75.3
top:MEM	19.9	19.9
top:WB	97.2	97.2

Figure 5: area analysis of the rv32i core
Module hierarchy	cumulated ALUTs used by the module and submodules	ALUTs used by the module
top	2139.0	143.6
top:EX	1769.9	1555.3
top:EX:clmul	147.8	147.8
top:EX:cpop	31.8	31.8
top:EX:ctz	19.0	19.0
top:EX:ctz	15.8	15.8
top:ID	32.3	32.3
top:IF	76.2	76.2
top:MEM	19.6	19.6
top:WB	97.4	97.4

Figure 6: area analysis of the rv32ib core, with a 4-cycle clmul
??? Figure 7: area analysis of the rv32ib core, with a single cycle clmul
## further work
The main contribution of this project is the verification and implementation of the rv32ib PAF core, as an exploration of the open source verification tool riscv-formal. It is to note that although the bug hunting verification mehodology is very useful in practice, it des not provide a complete correctness proof.
Further work can be done to fully prove the core, using unbounded model checking or theorem proving methods. Besides, as briefly discussed in the last section, the implementation can be improved. The area and timing analysis lead highlight the following potential improvements:
- better decoding in the ID stage to decrease the area.
- the addition of a pipeline stall when a byte load or a half-word load instruction is followed by JALR to improve the critical path.
- the addition of a new pipeline stage to improve the critical path.
### riscv-formal
riscv-formal is a promising open-source RISC-V bounded model checking verification tool. Though it lacks of support for multicore architechtures.
### PAF core
As stated in the synthesis analysis section, the PAF core implementation is to be imprpoved, by working on:
- a better decoding in the ID stage to decrease the area.
- the addition of a pipeline stall when a byte load or a half-word load instruction is followed by JALR to improve the critical path.
- the addition of a new pipeline stage to improve the critical path.
It also lacks of an interrupt mechanism.
1. M. Sheeran, S. Singh, and G. Stålmarck, ‘Checking Safety Properties Using Induction and a SAT-Solver’, in Proceedings of the Third International Conference on Formal Methods in Computer-Aided Design, 2000, pp. 108–125.
2. J. R. Burch and D. L. Dill, ‘Automatic Verification of Pipelined Microprocessor Control’, in CAV, 1994.
3. J. L. Hennessy. Designing a computer as a microprocessor: Experience and lessons from the MIPS 4000. A lecture at the Symposium on Integrated Systems, Seattle, Washington, March 14, 1993.
4. Wagner I., Bertacco V., (2011). ‘Verification of a Modern Processor’. In ‘Post-Silicon and Runtime Verification for Modern Processors’ (p. 4). New York: Springer.
5. Post-Silicon and Runtime Verification for Modern Processors, Springer, by Ilya Wagner Valeria Bertacco, Springer Science+Business Media, LLC 2011
6. AMBA AXI and ACE Protocol Specification, ARM, 2011, pp. 37-42